Rotational Kinematics:  It’s Enough to Make Your Head Spin!

- A wheel rotates 3.00 times.  What is its angular displacement?

- If a 30.0 cm radius wheel rotates through 3.0 radians how far has it rolled?

- What is the angular displacement of the minute hand on a clock during a 30.0-minute interval.

- Three hours pass by.  What is the angular displacement of the Hour hand on the clock during this interval?

- A carnival ride rotates through 4.0 radians of angular displacement.  If the ride has a diameter of 4.0 meters, what is the path length that the passengers have moved in this time?

- A merry-go-round rotates 10 complete revolutions.  What path length has the passenger moved through if they are seated 2.0 meters from the ride’s center?

- Through how many radians has a 40.0 cm radius wheel rotated through if it has traveled 10.0 meters?

- A motor runs at 1200 rpm.  What is the angular speed of the motor?

- A wheel is observed to rotate 5 complete revolutions in 25 seconds.  What is its angular speed?

- What is the angular speed of the minute hand of any clock?

- What is the tangential velocity of a point at the equator of the earth?  (radius of earth = 6.37 x 106 meters)

- What is the angular velocity of a point at the equator of the earth?  (radius of earth = 6.37 x 106 meters)

- An automobile wheel rotates at 5.0x102 rpm.

  - If the wheel has a diameter of 1.0 meter, what is the velocity (m/s) of the automobile?

  - If the wheel is underinflated, its diameter is only 0.90 meters and rotates at the same speed.  What velocity will the car have?

- In order to travel at 20.0 m/s what angular speed must your tires have if your tires have a 0.80 m radius?

- A cyclist traveling at 5.0 m/s uniformly accelerates up to 10.0 m/s in 2.0 seconds.  Each tire of the bike has a 35 cm radius, and a small pebble is caught in the tread of one of them. What is the angular acceleration of the pebble during those two seconds?

- A flywheel speeds up uniformly from rest to 900.0 rpm in 2.0 minutes.

  - Find the angular acceleration.

  - Find the tangential acceleration of the rim if the flywheel has a 0.50 m radius.

- A CD player spins at 8590 rpm. If it starts from rest and has an acceleration of 450 rad/s2, how long does it take to reach full speed?

- A turntable is initially rotating at 0.40rad/s. The turn table then undergoes an angular acceleration of 0.085rad/s2 for 4.0s. Through what angle does the table rotate in this time?

- A turntable is initially rotating at 0.40rad/s. The turn table then undergoes an angular acceleration of 0.085rad/s2 for 4.0s. Through what distance does a point 12.0cm from the center of the table travel in this time?

- A car accelerates around a circular track. The track has a radius of 25.0m. The car starts at rest and accelerates to 20.0m/s in 8.00s.

a. Find the cars angular acceleration.

b. Find the cars tangential acceleration.

c. Find the cars centripetal acceleration at t=8.00s.

Answers:

- 1080o or 18.8 rads

- 0.90m

- π radians, 3.14radians

- 1.57 radians

- 8.0 m

- 130 m

- 25.0 radians

- 126 rad/s

- 1.3 rad/s

- 0.0017 rad/s

- 4.64 x 102 m/s

- 7.27 x 10-5 rad/s

- a. 26 m/s b. 24 m/s

- 25 rad/s

- 7.14 rad/s2

- a. 0.79 rad/s2 b. 0.39 m/s2

- 2.0 s

- 2.3rad

- 0.27m

- a. 0.10rad/s2	b. 2.5m/s2	c.16m/s2